## Slide 1: 8085-MICROPROCESSOR & IT'S WORKING
BY : MD SHAKIL ANSARI

## Slide 2: CONTENTS
INTRODUCTION
8085-BASIC FEATURES
PIN CONFIGURATION
8085-ARCHITECHTURE
REGISTER SET OF 8085
CONTROL SIGNALS OF 8085
8085- BUS STRUCTURE
INTERRUPTS OF 8085
USES OF 8085
CONCLUSION

## Slide 3: INTRODUCTION
The 8085 microprocessor is a programmable integrated device that has computing and decision making capability .
It is basically a multipurpose, clock-driven, register-based electronic device that read binary instructions from storage device and gives result after processing it. If we think at elementary level ,we can draw an analogy between a microprocessor and human brain as it works more likely as human brain.

## Slide 4: 8085-BASIC FEATURES
Few of the salient features of 8085 microprocessors are listed below...
It is an 8-bit microprocessor with a 40 digital pins.
It has 16 address lines/bus ,hence it can access 2^16=64kb of external memory.
It provides 8-bit I/O address to access 2^8=256 I/O ports.
It supports 74 addressing modes with five addressing modes viz.{ Immediate ,register ,direct ,indirect ,implicit }addressing modes.
It supports von Neumann architecture.
It provides 5 hardware interrupts viz. TRAP,RST 7.5,RST 6.5,RST 5.5 & INTR
It has I/O control unit which allows serial communication.
It comes with control signal pins viz. IO/M',RD',WR' which control the direction of data flow between the processor and memory and I/O devices

## Slide 5: PIN CONFUGURATION
The 8085 microprocessor comes with a set of 40 digital pins.
They are further subdivided into 6 groups based on their working.

## Slide 6: 8085-ARCHITECTURE
The 8085 microprocessor is a von Neumann designed based IC .Several parts of the architecture is listed below as functional group.
ALU
Timing and control unit
General purpose registers
Interrupt control unit
Instruction decoder and machine cycle encoder
Serial I/O control
Address Bus
Data Bus

## Slide 7: 8085-ARCHITECHTURE CONTD....

## Slide 8: REGISTER SET OF 8085
There are 6 general purpose register in 8085.They are used to store the data.
Apart from this,8085 also has some special purpose register which are used for special work.
General Purpose Register : B,C,D,E,H,L . All are of 8-bit capacity .They can be used in pairs (B-C,D-E,H-L) in order to store any 16-bit information like address of any memory location.
General Purpose Register : Stack pointer(SP) , Programme Counter(PC).They are all of 16 bit capacity.
Accumulator(8-bit): This is one of the most used registers of 8085.It holds one of the operands of any operation and also the result is stored by the accumulator.

## Slide 9: REGISTER SET OF 8085 contd..
Flag Register: It is a also of 8 bit which shows the status of the result of any arithmetical and logical operation.
Sign Flag: It(the MSB of the Flag REGISTER) is HIGH Only when the result of any arithmetic and logical operation turns out to be NEGATIVE.
Zero Flag: It is HIGH Only when the result of any arithmetic and logical operation turns out to be ZERO.
Auxiliary Flag: It is HIGH Only when there is a carry generated from the nibble of any 8-bit result.
Parity Flag: It is HIGH ONLY when the result of any operation contains even number of 1s.
Carry Flag: It is HIGH ONLY when the result of any operation contains a carry out of the MSB bit.

## Slide 10: CONTROL SIGNALS OF 8085
The 8085 microprocessor comes with 3 control signals which indicate the current status of the processor .They are...
IO/M'
RD'
WR'
They govern the direction of data flow within the processor and its peripherals .

## Slide 11: 8085-BUS STRUCTURE
The 8085 microprocessor comes with two types of buses
Address Bus (16 Bit):- carries address of memory locations . It is unidirectional
Data Bus(8 Bit):- carries data(raw materials) between processor and its peripherals .It is bi-directional.

## Slide 12: INTERRUPTS OF 8085
8085-Microprocessor deals with interrupt signals whenever required .Interrupts can be classified into various categories based on the parameters.
Hardware & Software interrupts: when the interrupts arise through any hardware pin ,that is known as Hardware interrupts. e. g- INTR, RST 7.5, RST 6.5, RST 5.5, TRAP
when the interrupts are inserted in between the programs in mnemonics form ,that is known as Software interrupts e.g- RST 0, RST 1, RST 2, RST 3, RST 4, RST 5, RST 6, RST 7.
Vectored and Non-Vectored Interrupts: Those interrupts which have fixed vector address (starting address of sub-routine) and after executing these, program control is transferred to that address.
Non-Vectored Interrupts are those in which vector address is not predefined. E.g - except INTR all interrupts are vectored.

## Slide 13: INTERRUPTS OF 8085 contd..
Maskable and Non-Maskable Interrupts – Maskable Interrupts are those which can be disabled or ignored by the microprocessor .INTR, RST 7.5, RST 6.5, RST 5.5 are maskable interrupts in 8085 microprocessor.
Non-Maskable Interrupts are those which cannot be disabled or ignored by microprocessor. TRAP is a non-maskable interrupt.

## Slide 14: USES OF 8085
Microprocessors now a days is an essential part of any electronic ,computing and decision making device.
Some of their application are listed below..
Traffic light control system
Communication system
Calculators
Embedded part of multi-function environment.

## Slide 15: CONCLUSION
Going through this PPT ,we can draw a conclusion that microprocessors are everywhere .They are integral part of many electronic-computing devices .Although 8085 microprocessor are almost obsolete but this is the fundamental and one of the ancestral processors .Learning the features and functionality of 8085 is very essential to understand some advanced processors like pentium .